Recovering CMM when it boots only to VxWorks Boot.

If CMM does not boot (use EMP for restoring images)

Convention - bold type should be the settings used.

- Place a jumper on J343 pins 1 & 2 (CMM-F80), or

  - Place a jumper on J15  pins 1 & 2 (CMM-F40), or

  - Place a jumper on J26 pins 1 & 2 (OS8800-CMM).

  - This will force the system to open access to the firmware boot code.

Note – usually there is a spare jumper available placed between pins 15 & 16 on the same row of pins noted above.

- Connect the Console cable, settings are 9600,8,N,1.

- Connect the EMP Ethernet cable to your Laptop/PC where the code is stored.

- Power on the OmniSwitch 7x00 or 8800.

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x1000, press enter until you get the [VxWorks Boot] prompt again,

- Type "@", to continue booting to Miniboot.

- From here you can use step #12, if the failure is due to unusable images in the certified directory, but the working directory has usable images.  If the images need to be restored to both directories skip to step #14.

- [Miniboot]-> setNextRunningVersion 2  - skip to step #35

- [Miniboot]-> sysModifyBootParameters

- Boot > boot empipaddr x.x.x.x

    - (this address must be able to reach the ftp device)

- Boot > boot empnetmask ffffff00

- Boot > commit file

  - WARNING: Changes have not yet been committed to the running system.

- Would you like to commit your changes to the file anyway? (y/n) y

  - Boot param changes written to the NVRAM and to the file /flash/boot.params'.

  - WARNING: Your changes will take effect at the next system boot.

- Boot > exit

  - WARNING: Changes have not yet been committed to the running system.

- Would you like to exit anyway? (y/n) y

- [Miniboot]-> reboot - you need to reboot before the next step

- [Miniboot]-> sysStartNetwork

- [Miniboot]-> sysFtp

- Host : x.x.x.x

- Name : anonymous

- Password: emailname@mycomany.com (this will not be displayed)

- ftp> prompt

- ftp> bin

- ftp> has

- ftp> cd to the location where the software files are stored.

- ftp> lcd /flash/certified

- ftp> mget *.img

- ftp> lcd /flash/working

- ftp> mget *.img

- ftp> bye

- [Miniboot]-> reboot

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x0, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to system.

- login : admin

- password : ********

- Power down the unit and remove the J343 or J15 or J26 jumper.