# Updating OmniSwitch 8800 miniboot code.

For upgrading a running system’s miniboot, please see “Updating Miniboot to a Newer Version”. This procedure is to be run on Primary (Single) CMM configurations only. Do not use this procedure with the switch configured for redundancy.

## Please note the following supported versions of miniboot

8800 running 5.1.3 or lower code requires miniboot version 5.1.1.200.

## If CMM does not boot (uses EMP)

- Place a jumper on J26 pins 1 & 2

This will force the system to open access to the firmware boot code.

- Connect the Console cable, settings are 9600,8,N,1.

- Connect the EMP Ethernet cable to your Laptop/PC where the code is stored.

- Power on the OmniSwitch.

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x1000, press enter until you get the [VxWorks Boot] prompt again,

- Type "@", to continue booting to Miniboot.

- [Miniboot]-> sysModifyBootParameters

- Boot > boot empipaddr x.x.x.x

(this address must be able to reach the ftp device)

- Boot > boot empnetmask ffffff00

- Boot > commit file

WARNING: Changes have not yet been committed to the running system.

- Would you like to commit your changes to the file anyway? (y/n) y

Boot param changes written to the NVRAM and to the file /flash/boot.params'.

WARNING: Your changes will take effect at the next system boot.

- Boot > exit

WARNING: Changes have not yet been committed to the running system.

- Would you like to exit anyway? (y/n) y

- [Miniboot]-> reboot – you need to reboot before the next step

- [Miniboot]-> sysStartNetwork

- [Miniboot]-> sysFtp

- Host : x.x.x.x

- Name : anonymous

- Password: emailname@mycompany.com (this will not be displayed)

- ftp> prompt

- ftp> cd OS8800_code/miniboot

- ftp> lcd /flash

- ftp> mget *

- ftp> cd ..

- ftp> lcd /flash/certified

- ftp> mget *.img

- ftp> lcd /flash/working

- ftp> mget *.img

- ftp> bye

- [Miniboot]-> sysUpdateBootrom

- [Miniboot]-> sysUpdateMiniboot(0)

- [Miniboot]-> sysUpdateMiniboot(1)

- [Miniboot]-> sysBoardReset

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x0, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to system.

- login : admin

- password : ********

- -> rm bootrom.bin

- -> rm miniboot.default

- -> rm miniboot.backup

- -> configuration snapshot AAA

- -> cp asc.1.snap /flash/certified

- -> cp asc.1.snap /flash/working

- -> rm asc.1.snap

- Power down the unit and remove the J26 jumper.

For upgrading an existing systems miniboot, please see second procedure.

This procedure is based on the workings of the OmniSwitch 8800. If you any questions regarding this procedure, please contact Alcatel eBND Customer Service department at 1-800-995-2696.

# Updating Miniboot and Bootrom to Newer Version.

- Place a jumper on J26 pins 1 & 2

- Connect the Console cable, settings are 9600,8,N,1.

- Connect the EMP Ethernet cable to the CS Test Network.

- Power on the Unit – allow the system to boot to running code.

- login : admin

- password : *******

- -> ftp x.x.x.x

- Name : anonymous

- Password: emailname@mycompany.com (this will not be displayed)

- ftp> cd OS8800_code\microcode

- ftp> lcd /flash

- ftp> prompt

- ftp> mget *

- ftp> bye

- -> reload

- Confirm Restart? (y) y

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x1000, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to Miniboot.

- [Miniboot]-> sysUpdateBootrom

- [Miniboot]-> sysUpdateMiniboot(0)

- [Miniboot]-> sysUpdateMiniboot(1)

- [Miniboot]-> sysBoardReset

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the VxWorks Boot],

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x0, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to system.

- login : admin

- password : *******

- -> rm bootrom.bin

- -> rm miniboot.default

- -> rm miniboot.backup

38. Power down the unit and remove the J26 jumper.

This procedure is based on the workings of the OmniSwitch 8800. If you any questions regarding this procedure, please contact Alcatel eBND Customer Service department at 1-800-995-2696.

# Updating Bootrom to Newer Version.

- Place a jumper on J26 pins 1 & 2

- Connect the Console cable, settings are 9600,8,N,1.

- Connect the EMP Ethernet cable to the CS Test Network.

- Power on the Unit – allow the system to boot to running code.

- login : admin

- password : *******

- -> ftp x.x.x.x

- Name : anonymous

- Password: emailname@mycompany.com (this will not be displayed)

- ftp> cd OS7_code\microcode

- ftp> lcd /flash

- ftp> prompt

- ftp> mget *

- ftp> bye

- -> reload

- Confirm Restart? (y) y

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x1000, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to Miniboot.

- [Miniboot]-> sysUpdateBootrom

- [Miniboot]-> sysBoardReset

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the VxWorks Boot],

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x0, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to system.

- login : admin

- password : *******

- -> rm bootrom.bin

- Power down the unit and remove the J26 jumper.

This procedure is based on the workings of the OmniSwitch 8800. If you any questions regarding this procedure, please contact Alcatel eBND Customer Service department at 1-800-995-2696.