Updating OmniSwitch 8800 Bootrom code

This procedure is to be run on Primary (Single) OS-8800’s only. Do not use this procedure with the switch in redundant configurations.

- Power on the switch - allow the system to boot to running code.

- login : admin

- password : switch (if it has not been previously changed)

- -> show hardware info

- look for the line: BootROM version: (it should say 5.1.1.200.R01)

- -> ftp x.x.x.x (ftp to the location where you stored the new files)

- Name : anonymous

- Password: emailname@yourcompany.com (this will not be displayed)

- ftp> cd to the directory on the server where the files are located.

- ftp> lcd /flash

- ftp> prompt

- ftp> bin

- ftp> hash

- ftp> get bootrom.bin

- ftp> bye

- -> reload

- Confirm Restart? (y) y

- Stop the auto-boot countdown sequence by ”y”.

Note – If the above option to interrupt the boot sequence does not show up due to CMM jumper settings then do the following, otherwise skip to step 19-

  - dshell
Certified: [Kernel]->bootChange
'.' = clear field; '-' = go to previous field; ^D = quit
boot device : flash
processor number : 0
host name : OmniSwitchCmm
file name :
inet on ethernet (e) : 192.168.1.1:ffffff00
inet on backplane (b) :
host inet (h) : 192.168.10.1
gateway inet (g) : 192.168.1.254
user (u) : OmniSwitchUser
FTP password (pw) (blank = use rsh) : OmniSwitchPassword
flags (f) : 0x0 0x1000 ** to stop in MiniBoot
target name (tn) : OmniSwitch
startup scrIPt (s) :
other (o) : lnPci
serial (console) baud (cb) : 9600
serial (console) parity (cp) : none
serial (console) stopbits (cs) : 1
serial (console) wordsize (cw) : 8
serial (console) mode (cm) : modemControlOff
memory size (ms) (64 or 128) : 0
value = 0 = 0x0
Certified: [Kernel]->exit
6 Software Upgrade, BootROM and MiniBoot update for 6600, 7000 & 8800 series
August 11, 2003 - rev. A06 Alcatel eND Customer Support
** Now reboot the system.
-> reload
Confirm Reload (Y/N) : y

Now proceed with step 24 at the Miniboot prompt

- Type "y"es so the boot will enter the [VxWorks Boot].

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x1000, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to Miniboot.

- [Miniboot]-> sysUpdateBootrom

22-a When the update process works correctly, here is the output:

[Miniboot]->sysUpdateBootrom

Erasing bootrom...

Programming bootrom with '/flash/bootrom.bin'...

Bootrom updated!!!

value = 0 = 0x0

[Miniboot]->

22-b When the update process does NOT work correctly, here is the output:

[Miniboot]->sysUpdateBootrom

Erasing bootrom...

Error erasing bootrom.

Delaying 5 seconds before retry...

*** WARNING: Retry no. 1.

Erasing bootrom...

Error erasing bootrom.

Delaying 5 seconds before retry...

*** WARNING: Retry no. 2.

{ootrom NOT updated!!!

value = -1 = 0xffffffff = udbinfo + 0xff93033f

[Miniboot]->

If it is not working, retry between 1 to 4 times and it should work at the end.

Do not reload the switch if the upgrade process failed!

Keep issuing “sysUpdateBootrom” command until “Bootrom updated!!!” message.

- [Miniboot]-> sysBoardReset

- Stop the auto-boot countdown sequence by ”y”.

- Type "y"es so the boot will enter the VxWorks Boot],

- Type "c" to enter configuration.

- Press enter to accept the default entries until you see the flags(f) option.

- Type 0x0, press enter until you get the [VxWorks Boot] prompt again.

- Type "@", to continue booting to system.

- login : admin

- password : switch

- -> rm bootrom.bin

- ->	show hardware info

- look for the line: BootROM version: (it should now say 5.1.4.67.R01)

This procedure is based on the workings of the OmniSwitch 8000.

If you any questions regarding this procedure, please contact Alcatel eBND Customer Service department at 1-800-995-2696.

It is recommended that down-time be scheduled to upgrade each CMM individually in a non-redundant fashion as described above.  If a redundant CMM upgrade procedure is required please contact Customer Service for more information.